## Slide 1: COMPUTER AIDED SHIP DESIGN
PROPELLER DRAWING PROGRAM

## Slide 2: AIM
To develop a program for defining the geometry and drawing all views of a propeller blade in an easily accessible format (autoCAD).

## Slide 3: PROGRAMMING LANGUAGE
AUTOLISP
AutoLISP is a dialect of the old LISP language. LISP stands for List Processing.
AutoLISP is instrumental in automating a large number of repetitive tasks.
This is not a very advanced language like C++ or java. It lacks facilities for advanced programming concepts like object oriented programming.
Advanced file manipulation operations like random access is also not available. But for the specific use of automating autoCAD, this language is upto mark.

## Slide 4: WHY AUTOLISP?
AutoLISP is integrated into most CAD packages like autoCAD.
Thus, we need not install any dedicated development environments or compilers.
A great advantage is that output can be obtained in universally compatible CAD formats like DWG, DXF, etc. This was a major incentive in choosing AutoLISP over traditional languages like C++ or Visual BASIC.

## Slide 5: Program demonstration
SYSTEM REQUIREMENTS: Any version of autoCAD.

## Slide 6: HOW TO OBTAIN?
Visit http://code.google.com/p/acadprop
Contact us.

## Slide 7: SOURCE FILES
In the package, there are 5 files:
    1 source code (prop.lsp)
    3 data files (.txt)
    1 readme
Extract all files to d:/
IMPORTANT: all files must be in D:/ itself and not in any folders

## Slide 8: METHODOLOGY
START
INPUT Z,D, P/D, AE/AO, RAKE ANGLE (θ)
CHOOSE OFFSET BASED ON Z
OPEN OFFSET (AS PERCENTAGE) FILE AND GENERATE EXPANDED OFFSETS
GENERATE SECTION OFFSETS
DRAW EXPANDED BLADE WITH SECTION
CALCULATE VALUE OF C AND ANGLE OF ARC FOR DEVELOPED VIEW (using p/2π and r/cosφ
CALCULATE ANGLE FOR PROJECTED VIEW BY TAKING ANGLES FROM PROJECTIONS ON TRANSVERSE AND LONGITUDINAL PERPENDICULARS

## Slide 9: METHODOLOGY
CONVERT POLAR COORDINATES TO RECTANGULAR COORDINATES (x=rcosφ & y=rsin φ)
CALCULATING PROJECTED LENGTH AND THE ANGLE
DRAW GENERATOR LINE AT DISTANCE D FROM EXPANDED VIEW
DRAW AN ARC AT EVERY 0.1R DISTANCE
WRAP THE PROJECTION LENGTH ON EACH ARC USING THE PROJECTION ANGLE AND RADIUS
REPEAT SAME PROCEDURE FOR LONGITUDINAL PROJECTED VIEW
DRAW A CIRCLE AT P/2π DISTANCE FROM CIRCLE CENTRE (TO GENERATE AN ELLIPSE)

## Slide 10: METHODOLOGY
WRAP THE PROJECTED LENGTH ON THE ELLIPSE TO GENERATE DEVELOPED VIEW
DRAW SPLINES FOR DEVELOPED AND PROJECTED
DRAW SIDE VIEW USING RAKE ANGLE (θ) AND SECTION THICKNESS
OUTLINES AND TEXTS
MARGIN BOX
STOP

## Slide 11: DEMO

## Slide 12: THINGS TO NOTE
Automated Scaling
Run time memory for Input
Complete name plate with date

## Slide 13: VARIABLES AND FUNCTIONS
Thk : thickness of each section.
Lengths: length of each section
Length_le: length to leading edge
Maxthkpnt: distance of max thickness from GL
(initialise)
(read2array) Read from file to array
(makecoord) convert into coordinate
(getx) (gety) Get x,y from coordinate

## Slide 14: REAL LIFE APPLICATIONS
For fast design of Propellers
As a teaching aid (specially 5th Sem. Propulsion of Ships)

## Slide 15: POSSIBLE IMPROVEMENTS
Include a Graphical User Interface
Make other series of propeller data available
Convert data files into excel sheets from txt files.

## Slide 16: POTENTIAL OF AUTOLISP
Many uses for a draftsman/designer to automate repetitive tasks like naming and numbering drawings
Can generate complete lines plan from body plan.
Assist in fairing of Lines plan.

## Slide 17: Thank you!
PRESENTED ON 13TH OCTOBER 2009